## Slide 1: WAVEGUIDE MAGIC TEE WITH WR650
Group - 08
AP20110020018_ Dattasai. R
AP20110020023_ Shanmukh. T.S
AP20110020004_ Syed Fazila
AP20110020039_ Devipriya.N

## Slide 2: INTRODUCTION
A Magic Tee is a 3 DB coupler used in microwave systems. The magic tee comes from the way it prevents signals from propagating between certain ports under specific conditions. This allows it to be used as a duplexer; for instance , it can be used to isolate the transmitter and receiver in a radar system while sharing the antenna. In practical examples, it is used to both isolate circuits and mix signals, for instance in a rader.
The Magic Tee is a combination of E and H plane tees. Arm 3 forms an H-plane tee with arms 1 and 2. Arm 4 forms an E-plane tee with arms 1 and 2. Arms 1 and 2 called the collinear arms. Port 3 is called the H-port. Port 4 is called the E-plane port.

## Slide 3: DEVICE BACKGROUND

## Slide 4: WORKING PRINCIPLE
A Magic tee(EH plane tee) is able to perform an apparently magical function, which is to allow for energy going into the E and H plane ports to be divided between the two collinear ports while isolating the E and h plane ports and the two collinear ports from each other.
Different than other power dividers or couplers, The magic-tee performs different functions at the E plane and H plane ports. The H plane port will present the same phase at both collinear ports, The E plane port present 180 degree phase referenced to the different collinear ports. This function of a magic tee is also symmetric, And it will split the energy going into a collinear port to both the E and H plane port. Hence, signals going into the collinear ports will be simultaneously divided, symmed at the H plane port, and differenced at the E plane port.

## Slide 5: APPLICATIONS
Magic Tee can be used to measure impedance by connecting a null detector to the E plane port.
Magic Tee is used as duplexer.
Magic Tee is used as mixer.
Magic Tee junction is also called as Microwave Bridge, Microwave discriminator.

## Slide 6: STUDY RESULTS
In this Magic Tee we got the combination of E and H plane tees parameters.

## Slide 7: CONCLUSION
So, finally the conclusion is the isolation between the E plane and H plane ports is wide band and is as perfect as is the symmetric of the device. The isolation between the collinear ports is however limited by the performance of the matching structure.

## Slide 8
THANK YOU